## Slide 1: Microsoft Lync 2010 : Lync & the Enterprise Network
Vakhtang Assatrian Victor Kochetkov
Voice TSP, WW Target Accounts Voice Architect
Microsoft
SESSION CODE: EXL305

## Slide 2: Agenda ‘what makes this session interesting’
Voice Evolution
Defining Voice Quality, Success and Challenges
Network Considerations & Impact
  Bandwidth Requirements
  Call Admission Control
  QoS, VLANs
  Session Resiliency

## Slide 3: Objective
Better understand Lync™ 2010 and the Enterprise Network
In scope: QoE, Bandwidth, Codecs, Forward Error Correction(FEC), Bandwidth Estimation, Call Admission Control (CAC), Differentiated Services Code Point (DSCP), Link Layer Discovery Protocol (LLDP), Virtual LANs (VLANs)
Monitoring, Partners, OSI, Resiliency.
Out of Scope: Everything Else

## Slide 4: Evolution of Voice Transport
Connection signalled based on destination number. Connection remains up for the duration of call
10.1.1.1 | 10.1.2.1
Voice
Caller: Party A 10.1.1.1
Called: Party B 10.1.2.1
Caller: Party A
Called: Party B
E1
E1
10.1.2.1 | 10.1.1.1
Voice
Class 5
Class 5
Class 4
Class 4
Each packet contains source + destination addresses packets are routed by hop, flow or destination.

## Slide 5: What Defines Voice Quality?
Call Reliability
  Calls get established as expected
  Calls do not drop mid-way through
Audio Quality
  Meeting users needs for how audio sounds within a call
Who Matters
  End user quality of experience
    Can I make voice calls successfully?
  Admin quality of life
    Can I discover, diagnose, and resolve voice quality issues effectively?

## Slide 6: Mean Opinion Scores (MOS)
Uses humans for the testing (very subjective)
MOS-LQ: Listening Quality
  Measures quality of audio for listening
  Does NOT account for bidirectional effects, such as delay and echo
MOS-CQ: Conversational Quality
  Accounts for listening quality in BOTH directions
  Measures bidirectional effects
Rating | Speech Quality | Level of Distortion
5 | Excellent | Like standing next to the speaker
4 | Good | Just perceptible, not annoying
3 | Fair | Perceptible, minor annoyance
2 | Poor | Annoying but will not hang up
1 | Unsatisfactory | I would hang up

## Slide 7: Perceptual Evaluation of Speech Quality
PESQ
PESM – Perceptual Speech Quality Measure
  Predecessor to PESQ
Uses algorithms for the testing (consistency)
  Objective – will produce same results

## Slide 8: What Constitutes “Good” Voice Quality?
Starting point for expectations for most users is the desktop PABX phone
  High dial-tone availability
  Narrow band audio
“Good” Voice Quality is highly personal and context sensitive
  Up to a point, users will accept lower Voice Quality given other advantage
    Cellular phones trade mobility for lower call reliability
    Internet VoIP users trade price for audio quality
Bottom Line: Users not noticing Voice Quality issues is what defines success

## Slide 9: Understanding The Challenges
Failed Calls
Dropped Calls
One Way Audio
Echo
Noise
Low Volume
Delayed Audio
Broken Up Audio
Distorted Audio
Network
Core Performance
Call Reliability
Audio Quality
Voice Quality Issues
Gateways
Devices

## Slide 10: Network Performance Goals
Further performance deviates from these goals the more likely users experience poor voice quality
For great Voice Quality pair good network performance with:
  UC Logo certified Devices and Gateways
  Server roles running on recommended spec hardware
Network Conditions | Acceptable Quality | Optimal Quality
Inter-arrival packet jitter (avg) | ≤ 10ms | ≤ 5ms
Inter-arrival packet jitter (max) | ≤ 80ms | ≤ 40ms
Packet loss rate (avg) | ≤ 10% | ≤ 2%
Network latency RTT | ≤ 200ms | ≤ 120ms

## Slide 11: The Open Systems Interconnection (OSI) Model
Layer | Definition
Seven | 
Six | 
Five | 
Four | 
Three | 
Two | 
One | 
Physical
Data Link
Network
Transport
Session
Presentation
Application
“lol rofl”
….a way of sub-dividing a communications system into smaller parts called layers.
A layer is a collection of similar functions that provide services to the layer above it and receives services from the layer below it.
On each layer, an instance provides services to the instances at the layer above and requests service from the layer below. - Wikipedia

## Slide 12
Application | Partners/Apps
Presentation | Resiliency
Session | CAC
Transport | Media Ports
Network | DSCP
Data Link | LLDP & VLANs
Physical | Bandwidth

## Slide 13
Application | 
Presentation | 
Session | 
Transport | 
Network | 
Data Link | 
Physical | 
Bandwidth

## Slide 14: Anatomy of a UC Audio Session
1
2
3
4
5
1
4
2
5
3
SRTP / RTCP
SIP
Perfect
Network

## Slide 15: Anatomy of a UC Audio Session
1
2
3
4
2
3
Forward Error Correction
4
5
1
2
3
4
2
3
4
5
1
4
2
5
1
2
4
5
1
2
3
4
5
Poor
Network
SRTP / RTCP
SIP

## Slide 16: Bandwidth
Media Endpoints detect & manage distribution of available BW
  Prioritize Audio first and distribute remaining bandwidth to Application Sharing, Video, and File Transfer
  Choose best quality Audio codec, video resolution/frame rate for available BW
  Adapt to network & change codecs to optimize experience during a session
Bandwidth requirements determined by
  Codec choice: Microsoft RT-Audio & RT-Video, G.711, G.722, etc.
  Network performance: Using FEC for redundant audio encoding
  Channel Activity: Voice activity and video content

## Slide 17: Lync™ 2010 on a bad network
demo

## Slide 18: Bandwidth - Planning
Modality | Codec | Typical BW | Max w/o FEC | Max w/FEC
P-t-P audio | RTA-W | 39.8 | 62 | 91
P-t-P audio | RTA-N | 29.3 | 44.8 | 56.6
PSTN audio | RTA-N | 30.9 | 44.8 | 56.6
PSTN audio | G.711 | 64.8 | 97 | 161
audio conf | G.722 | 46.1 | 100.6 | 164.6
audio conf | Siren | 25.5 | 52.6 | 68.6
Video | RTV - CIF | 220 | 260 | 
Video | RTV - VGA | 508 | 610 | 
Video | RTV - HD | 1210 | 1510 | 
Video | RTV - Pano | 269 | 360 | 
One-way traffic including media, typical activity, RTCP.
For planning in a well managed, right-sized network, use Max BW w/o FEC.
If the network will be constrained and you want to preserve quality, use Max BW with FEC.
When understanding how much bandwidth at any given time is being used, use the Typical BW numbers. Not for planning, as usage will be greater at times.
All voice numbers are based on 20ms sample
For Video: FEC built into the payload bitrate

## Slide 19: Bandwidth - Application Sharing
Application sharing bandwidth consumption dependent on session content and screen resolution
TCP based sessions with built-in congestion control
Traffic is bursty in nature
End user policy limits to cap spikes
Modality | Average bandwidth | Planned Maximum bandwidth
Application sharing using Remote Desktop Protocol (RDP) | 434 Kbps sent per sharer | 938 Kbps sent per sharer
Application sharing using Compatibility Conferencing service | 713 Kbps sent per sharer 552 Kbps received per viewer | 566 Kbps sent per sharer 730 Kbps received per sharer
Chart: Kilobits/sec sent by Sharer

## Slide 20: Audio/Video Bandwidth Controls
End User maximum allowed bandwidth per modality
  Applied whether or not bandwidth is available
  Configured via in-band provisioning at sign-in
Parameter | Default in Kb | PowerShell Command
Audio Bit Rate | 200 | Set-CsConferencingPolicy (AudioBitRateKb parameter)
Video Bit Rate | 50,000 | Set-CsConferencingPolicy (VideoBitRateKb parameter)
App Sharing Bit Rate | 50,000 | Set-CsConferencingPolicy (AppSharingBitRate parameter)
File Transfer Bit Rate | 50,000 | Set-CsConferencingPolicy (FileTransferBitRate parameter)
Parameter | Default Value | PowerShell Command
MaxVideoConferenceResolution {CIF. 352 x 288 or VGA 640 x 480} | VGA | Set-CsConferencingPolicy (MaxVideoConferenceResolution <CIF ¦ VGA>)
Parameter | Default Value | PowerShell Command
MaxVideoRateAllowed | VGA | Set-CsMediaConfiguration (MaxVideoRateAllowed <CIF250K, ¦ VGA600K ¦ Hd720p15M >)

## Slide 21: Lync™ 2010 Bandwidth Planning Tool
demo

## Slide 22
Application | 
Presentation | 
Session | 
Transport | 
Network | 
Data Link | 
Physical | Bandwidth
LLDP & VLANs

## Slide 23: LLDP & VLANs
LLDP-MED – Link Layer Discovery Protocol for Media Endpoint Devices
  Delivers Location information (switch and port) & VLAN ID to IP phones
  Lookup in Location Information Server for Location (used for E.911)
  Network switch must support IEEE 802.1AB and ANSI/TIA-1057
VLANs
  Great for address space management when deploying large number of phones
  Can use DHCP (Corp server or Lync ) if LLDP is not available
Two technologies that are for the IP phones only
  No native Windows driver for LLDP
  VLANs have _all_ traffic go onto the network

## Slide 24
Application | 
Presentation | 
Session | 
Transport | 
Network | 
Data Link | LLDP & VLANs
Physical | Bandwidth
DSCP

## Slide 25: DSCP – Differentiated Services Code Point
…AKA DiffServ
Recommended:
When Right Provisioning not possible and on Constrained WAN Links (pair with WAN bandwidth policies)
Prioritization already deployed for other VoIP solution
Your Friendly IPv4 packet

## Slide 26: DSCP
Windows® 7 and Windows Vista ®
  Lync users only use Windows Policy based QoS to mark based on application and port ranges
Lync IP Phones mark packets at endpoints
Windows XP® and Mac
  Mark at router based on port ranges only (or use Generic QoS)

## Slide 27: DSCP
Example “Fully Managed” Network Deployment
Media Type | Per Hop Behavior | Queuing and Dropping | Notes:
Audio | EF (DSCP 46) | Priority Queue | Low loss, low latency, low jitter, assured bandwidth Pair with WAN Bandwidth Policies on constrained links
Video | AF41 (DSCP 34) | BW Queue + DSCP WRED | Class 4. Low drop priority. Pair with WAN Bandwidth Policies on constrained links
SIP Signaling | CS3 | BW Queue | Class 3. Bandwidth allocation should be sufficient to avoid drops
App Sharing | AF21 (DCSP 26) | BW Queue + DSCP WRED | Class 2. Low drop priority. Pair with End User Policy Caps
File Transfer | AF11 (DSCP 10) | BW Queue + DSCP WRED | Class 1. Low drop priority. Pair with End User Policy Caps
More info @ Cisco Implementing Quality of Service Policies with DSCP

## Slide 28
Application | 
Presentation | 
Session | 
Transport | 
Network | DSCP
Data Link | LLDP & VLANs
Physical | Bandwidth
Media Ports

## Slide 29: Media Port Separation
If the client isn’t trusted, unique DSCP marking is achievable with non-overlapping port ranges for each modality and marking packets at router.
Monitor network traffic for each modality supported by Lync.
Lync Servers require separate port ranges for all modalities
  Audio port range applies to all audio servers; AV MCU, Mediation Server, Conferencing Services (CAA/PVA), Response Group Service (RGS), Call Park Server (CPS)
  Video Port range applies to AV MCU
  Application sharing port range applies to AS MCU
Suggest making Client audio/video port ranges subset of Server port range (simplify router configuration)
  Example: Server audio port range = 49,152 – 57,500, Client audio port range = 57,480 – 57,500

## Slide 30
Application | 
Presentation | 
Session | 
Transport | Media Ports
Network | DSCP
Data Link | LLDP & VLANs
Physical | Bandwidth
CAC

## Slide 31: Call Admission Control
Policy Server role in Lync Server implements CAC
  Admins configure logical sites based on groupings of subnets
  Enforce policies on links between sites
  Bandwidth available for audio, video
WAN link bandwidth policies
  Applied dynamically when session crosses network link with policy set
  Limits the session to a maximum allowed bandwidth level
  Re-route or fail session when bandwidth not available
Seamless support for roaming users on moving between different sites
Allows Internet to be used for overflow of traffic
  Avoid PSTN call charges
  Support alternate path & failover of video sessions

## Slide 32: Example Scenario
CAC Profile Type | WAN Link Per Session Audio Limit | Available Audio | WAN Link per Session Video Limit | Available Video
Optimized for Session Count (w/ Wide Band P2P) | 60 Kbps | RTAudio NB + FEC Siren + FEC RTAudio WB (no FEC) | 350 Kbps | RTVideo – CIF (15fps) RTVideo – Pano (15fps)
Balanced | 95 Kbps | (Above plus) RTAudio WB + FEC G.711 (no FEC) G.722 (no FEC) | 600 Kbps | (Above plus) RTVideo – VGA (30fps)
Optimized for Quality | 165 Kbps | (All Above plus) G.711 + FEC G.722 + FEC | 1500 Kbps | (All Above plus) RTVideo – HD (30fps)
Sydney
Melbourne
WAN Link Policy:
Audio Session Limit = 60 Kbps
RT Audio WB (No FEC)

## Slide 33: Example Scenario
CAC Profile Type | WAN Link Per Session Audio Limit | Available Audio | WAN Link per Session Video Limit | Available Video
Optimized for Session Count (w/ Wide Band P2P) | 60 Kbps | RTAudio NB + FEC Siren + FEC RTAudio WB (no FEC) | 350 Kbps | RTVideo – CIF (15fps) RTVideo – Pano (15fps)
Balanced | 95 Kbps | (Above plus) RTAudio WB + FEC G.711 (no FEC) G.722 (no FEC) | 600 Kbps | (Above plus) RTVideo – VGA (30fps)
Optimized for Quality | 165 Kbps | (All Above plus) G.711 + FEC G.722 + FEC | 1500 Kbps | (All Above plus) RTVideo – HD (30fps)
Sydney
Melbourne
Internet
WAN Link Policy:
Audio Session Limit = 60 Kbps
RT Audio WB (No FEC)

## Slide 34: Example Scenario
CAC Profile Type | WAN Link Per Session Audio Limit | Available Audio | WAN Link per Session Video Limit | Available Video
Optimized for Session Count (w/ Wide Band P2P) | 60 Kbps | RTAudio NB + FEC Siren + FEC RTAudio WB (no FEC) | 350 Kbps | RTVideo – CIF (15fps) RTVideo – Pano (15fps)
Balanced | 95 Kbps | (Above plus) RTAudio WB + FEC G.711 (no FEC) G.722 (no FEC) | 600 Kbps | (Above plus) RTVideo – VGA (30fps)
Optimized for Quality | 165 Kbps | (All Above plus) G.711 + FEC G.722 + FEC | 1500 Kbps | (All Above plus) RTVideo – HD (30fps)
Sydney
Melbourne
Internet
WAN Link Policy:
Audio Session Limit = 60 Kbps
RT Audio NB (+ FEC)

## Slide 35: CAC demo
demo

## Slide 36
Application | 
Presentation | 
Session | CAC
Transport | Media Ports
Network | DSCP
Data Link | LLDP & VLANs
Physical | Bandwidth
Resiliency

## Slide 37: Session Dialog Resiliency
Session Dialog Resiliency allows media to continue if signaling session is disrupted due to issues with Stateful Layer 3 middle boxes like Load Balancers or Signaling proxies.
During loss of signaling channel endpoint enter resiliency mode
  Some loss of functionality, e.g. hold/resume, conference roster, etc.
  Media session will continue
Automatic recovery of signaling channel whenever possible
(S)RTP/RTCP (UDP/TCP)
SIP (TCP)

## Slide 38: Session Dialog Resiliency
demo

## Slide 39
Application | 
Presentation | Resiliency
Session | CAC
Transport | Media Ports
Network | DSCP
Data Link | LLDP & VLANs
Physical | Bandwidth
Partners/Apps

## Slide 40: Partners
Lync™ 2010 supports broad interoperability with a well partner developed eco-system with
Networking equipment vendors
Load Balancer vendors
SIP Interoperability
Why Bother? See Gartner’s Debunking the Myth of the Single-vendor Network (public discussion here).
All docs linked from Network Infrastructure Roadmap

## Slide 41: Networking Infrastructure Partners
Enhance network infra. expertise & credibility of the MS UC solution
Bring to market best-in-class integrated UC/Networking solutions
Publish documentation to assist in optimization of the network:
Deliver differentiated UC + networking solutions through complementary product portfolios
Partner | OCS 2007 R2 | Lync
HP | Published | Published
Juniper | Published | Published
Brocade | Published | Published
Cisco | N/A | Testing to start July
Aruba | N/A | Published (WiFi)

## Slide 42: Load Balancer Vendors
Load balancer vendors qualified to work with Lync (here)
Vendor | Vendor’s Lync Page
A10 Networks | AX Series for Lync 2010 Overview and Deployment Guide (HW and SW LB)
AVANU/CAI Networks | CAI Networks' WebMux and Microsoft OCS 2007 R2 Solutions
Barracuda | Barracuda Load Balancer Deployment Guide
Brocade | Brocade Communications Microsoft UC Solutions
Cisco | Cisco Application Networking for Microsoft Office Communications Server Deployment Guide
Citrix Systems | Netscaler Developer Network (HW and SW LB)
F5 | F5 Solutions
Radware | Radware-Microsoft Alliance Highlights and Downloads

## Slide 43: SIP Interoperability partners
A broad set of vendors qualified to work with Lync 2010 (here):
  Direct SIP: Audiocodes, Cisco, Dialogic, Ferrari, Mitel, NET
  IP-PABX: Alcatel-Lucent, Avaya, Cisco
  SBA: Audiocodes, Dialogic, Ferrari, HP, NET
  SIP Trunking: BT, Colt, Global Crossing, Intelepeer, Interoute, Level 3, MyNetFone, Orange business services, Telenor, Speakup, Swisscom, Thinktel, Verizon Business, TDC
  More to come…

## Slide 44: In Review: Session Takeaways
Partners/Apps | Lync demonstrates broad open interoperability and adapts to heterogeneous networks
Resiliency | Recovers from bad networking/glitches much better than traditional hard-phone
CAC | CAC + Adaptive Media Stack + Re-routing over the internet
Media Ports | Optimize traffic at the workstation or the router. Separate traffic for modalities
DSCP | Mark the packets as they hit the wire from Lync clients
LLDP & VLANs | Working across heterogeneous network architectures
Bandwidth | Better quality of experience on any network with smart endpoints, management & monitoring across the network.

## Slide 45: Related Content
Lync Server Network Infrastructure Roadmap
Yankee Group White Paper: Network Considerations for OCS
Cisco Implementing Quality of Service Policies with DSCP
Lync 2010 Bandwidth Planning tool; Lync 2010 Capacity Planning tool
Lync 2010 Reskit tools
Aruba high-performance mobile access networks optimized for Lync

## Slide 46: Related Content
EXL202 | Microsoft Lync 2010: High Availability and Resiliency
EXL201 | Audio, Video and Web Conferencing Architecture and Experience
EXL306 | Interoperability, Integration with Legacy Systems
EXL309 | Microsoft Lync 2010: How to go big with voice
EXL312 | Setting Up and Deploying Microsoft Lync Server 2010 Edge Servers

## Slide 47: Enrol in Microsoft Virtual Academy Today
Why Enroll, other than it being free?
The MVA helps improve your IT skill set and advance your career with a free, easy to access training portal that allows you to learn at your own pace, focusing on Microsoft technologies.
What Do I get for enrolment?
Free training to make you become the Cloud-Hero in my Organization
Help mastering your Training Path and get the recognition
Connect with other IT Pros and discuss The Cloud
Where do I Enrol?
www.microsoftvirtualacademy.com
Then tell us what you think. TellTheDean@microsoft.com

## Slide 48: Resources
www.msteched.com/Australia
  Sessions On-Demand & Community
http:// technet.microsoft.com/en-au
  Resources for IT Professionals
http://msdn.microsoft.com/en-au
  Resources for Developers
www.microsoft.com/australia/learning
Microsoft Certification & Training Resources

## Slide 49
© 2010 Microsoft Corporation. All rights reserved. Microsoft, Windows, Windows Vista and other product names are or may be registered trademarks and/or trademarks in the U.S. and/or other countries.
The information herein is for informational purposes only and represents the current view of Microsoft Corporation as of the date of this presentation. Because Microsoft must respond to changing market conditions, it should not be interpreted to be a commitment on the part of Microsoft, and Microsoft cannot guarantee the accuracy of any information provided after the date of this presentation. MICROSOFT MAKES NO WARRANTIES, EXPRESS, IMPLIED OR STATUTORY, AS TO THE INFORMATION IN THIS PRESENTATION.