## Slide 2: Microsoft Lync 2010: Interoperability, Integration with Competition or Legacy
Victor Kochetkov
Voice Architect
Paul Dolley
Technology Strategist
Microsoft
EXL306

## Slide 3: Agenda
Brief summary of key principles: interop by design
Lync 2010 interoperability in practice
  Video room systems interoperability
  IP-PABX interoperability
    Media bypass support in Lync 2010
      What is it and how does it work
    Example: Interoperability with Cisco Unified Communications Manager (formally CallManager) and/or Cisco ISR
      Single site
      Multiple sites, central call control
    Migration approaches
Q&A

## Slide 4: Brief summary of key principles: interop by design

## Slide 5: Unified Communications Open Interoperability Program
Specific requirements for interoperability with Lync Server & Exchange Server Voice Mail
Testing requirements for qualifying interoperability with Lync Server & Exchange Server Voice Mail
Installation, set-up and configuration requirements via a Quick Start Guide
Release Notes with any known issues
Documented support process between Microsoft and the vendor
Enterprise-class standards for audio quality, reliability, and scalability

## Slide 6: UCI Forum Members

## Slide 7: Video room systems interoperability

## Slide 8
High quality video in every desktop
Improve the
meeting room
experience
Lync Video Strategy
High quality video in every desktop
  High resolution at low cost
  Single client experience
  Integration with applications
Embrace and lead interoperability
  Connect and integrate all legacy rooms (via gateways)
  Foster innovation in endpoints natively interoperable with Lync
  Develop on market standards and contribute to success of UCIF
Improve the meeting room experience
  Simplify and enrich user experience
  Expand reach and usage
  Improve productivity
Embrace
and Lead Interop

## Slide 9: Video Interoperability Program
announcement

## Slide 10: New: Video Interoperability Program
Allow partner solutions to make and accept video calls with Lync 2010 (or OCS 2007 R2)
  Direct registration to Lync for partner VTC/telepresence and/or MCU
  Gateways to connect any industry-standard VTC/telepresence and/or MCU to Lync
Process
  Partners submit solutions to Microsoft for qualification
  Qualified partner solutions will be listed on the Microsoft website
Requirements
  OCS 2007 R2:
    Enhanced security, point-to-point video, firewall traversal
  Lync 2010:
    Enhanced security, point-to-point video, firewall traversal
    RTVideo (HD), multiparty video on Lync MCU

## Slide 11
Secure registration
with “lowest common denominator” P2P
SIP registration
NTLM authentication or trusted server
Secure signaling (TLS)
Wideband audio
H.263 (CIF) interop
Presence publishing
Lync 2010: Video Interoperability Technical scope
  Firewall traversal and secure media for P2P
Firewall transversal
(ICE v19)
Secure calls (SRTP)
Seamless interop: partner video systems as highly capable Lync endpoints for rich, high quality multiparty calls between OC and partner solution
RTVideo – CIF, VGA, HD
CCCP for AVMCU support

## Slide 12: Partner Approaches
VTC Direct Registration
VTC register directly to Lync (or OCS 2007 R2)
Multiparty calls on Lync AVMCU (where supported)
VTC endpoints appear as contacts to Lync users
Users can take advantage of existing Lync functionality
  Click to call, drag and drop, right-click…
Committed partners:
  Polycom, Lifesize
Gateway/MCU
Gateway pass-through, Gateway/MCU
Users meet in virtual rooms for multiparty calls (hosted on partner MCU)
Virtual rooms appear as contacts in Lync
Legacy VCS/telepresence interoperability, multiple views, transcoding
Committed partners:
  Polycom, Lifesize, Radvision

## Slide 13: Cisco Telepresence Interoperability
As of today, Cisco does not have any qualified solution
  OCS 2007 R2: in process
  Lync: ask Cisco/Tandberg
Cisco/Tandberg planned interop through their gateways
  VCS gateway for signaling
  Tandberg “Advanced Media Gateway” for media transcoding
    Need both to get HD video
  Two more VCS (control, expressway) to work across firewall
Recommended approach: use partner gateway
  Polycom, Radvision

## Slide 14: Gateway Approach – Point to Point Call
Lync Server
Signaling
Video Codec
RTVideo
H.264
H.323
SIP/TLS
H.323 Endpoints
Lync
Gateway
Other
Lync
Media GW
Signaling Server
Registration, call routing, presence
Lync AVMCU
Registration, call routing, presence
Registration
RTVideo
SIP/TLS
Something is missing here… What is it?
That’s right,
no HW MCU

## Slide 15: MCU Virtual Room approach
Lync Server
Signaling
Video Codec
RTVideo
H.264
H.323
SIP/TLS
Lync
Gateway
Other
Lync
Media GW
Video Endpoint
Signaling Server
Registration, call routing, presence
Lync AVMCU
Registration, call routing, presence
Registration
RTVideo
SIP/TLS
HW MCU
Video Endpoint

## Slide 16: Video Endpoint Call Polycom & Tandberg
Required Components
Polycom
HDX
Tandberg
Endpoint
VCS
AMG (RTV Support)

## Slide 17: Polycom: Point-to-Point and MCU based interoperability with Lync
demo

## Slide 18: IP-PABX interoperability

## Slide 19: PABX Interoperability – 2 Approaches Client-Side & Server-Side Integration
Lync
PABX
Client API
Lync User
3rd Party Plug-in
Client Side Integration
Direct SIP
Lync
PABX
Lync user
PABX phone
user
Direct SIP Integration
SIP
Lync
PABX
Lync user
PABX phone
user
Gateway Integration
Legacy Protocol
Gateway
CSTA Gateway
Lync
PABX
Lync user
PABX phone
user
RCC Integration

## Slide 20: PABX Interoperability – 2 Approaches Client-Side & Server-Side Integration
Lync
PABX
Client API
Lync User
3rd Party Plug-in
Client Side Integration
No large-scale customer deployments (Pilots only)
Isn’t free, additional licenses may be required
Complex Integration
Harder to support, higher TCO
Disjointed user experience, less options

## Slide 21: PABX Interoperability – 2 Approaches Client-Side & Server-Side Integration
Lync
PABX
Client API
Lync User
3rd Party Plug-in
Client Side Integration
Direct SIP
Lync
PABX
Lync user
PABX phone
user
Direct SIP Integration
SIP
Lync
PABX
Lync user
PABX phone
user
Gateway Integration
Legacy Protocol
Gateway
CSTA Gateway
Lync
PABX
Lync user
PABX phone
user
RCC Integration

## Slide 22: PABX Interoperability – 2 Approaches Client-Side & Server-Side Integration
SIP
Lync
PABX
Lync user
PABX phone
user
Gateway Integration
Legacy Protocol
Gateway
Most basic form of interop – useful for PoC/Pilot
Allows Direct Calling
Not a long term UC solution
Also deployed on non SIP capable PABX during migration to Lync

## Slide 23: PABX Interoperability – 2 Approaches Client-Side & Server-Side Integration
Lync
PABX
Client API
Lync User
3rd Party Plug-in
Client Side Integration
Direct SIP
Lync
PABX
Lync user
PABX phone
user
Direct SIP Integration
SIP
Lync
PABX
Lync user
PABX phone
user
Gateway Integration
Legacy Protocol
Gateway
CSTA Gateway
Lync
PABX
Lync user
PABX phone
user
RCC Integration

## Slide 24: PABX Interoperability – 2 Approaches Client-Side & Server-Side Integration
CSTA Gateway
Lync
PABX
Lync user
PABX phone
user
RCC Integration
In/Outbound calling (hold, transfer, Caller ID)
Forward deskphone via Lync
Call via deskphone
Call via Lync
What You Get
What’s Missing
Escalate to multi-party audioconf
Videoconf
Receive calls at home, on the road
Synchronize Do Not Disturb
Escalate inbound call to desktop sharing
No delegation

## Slide 25: PABX Interoperability – 2 Approaches Client-Side & Server-Side Integration
Direct SIP
Lync
PABX
Lync user
PABX phone
user
Direct SIP Integration

## Slide 26: Direct SIP Integration Pain points in OCS 2007 R2
Interoperability via Direct SIP (OIP qualification)
  Very broad range of PSTN gateways, Direct SIP to IP-PABX
However, in R2 Direct SIP requires routing media through Mediation Server
  Not a significant problem for central sites
  But difficult in branches:
    Requires Mediation Servers in branches and/or
    Media tromboning (hairpin through the WAN to Mediation Server in central site)

## Slide 27
OIP qualified IP-PABX
PABX end-points
OCS pool
OCS end-points
Mediation Server
Media
Signaling
IP-PABX Interoperability in OCS 2007 R2 Direct SIP to IP-PABX

## Slide 28: IP-PABX Interoperability in Lync Direct SIP to IP-PABX with media bypass
OIP qualified IP-PABX
capable of bypass
PABX end-points
Lync pool with MS role
Lync end-points
Media
Signaling

## Slide 29: Lync 2010: Media Bypass What it is and benefits
Removes need for media transit via a server
  Signaling continues to transit through Mediation
    B2BUA: security demarc, interop…
  Media goes directly from Lync client to next hop (gateway, IP-PABX)
    Quality optimization (latency reduction, codec selection, media resiliency)
Based on location of Lync client
  Bypass only occurs if client is “local” to next hop
    G.711 direct – optimized for LAN-like conditions; SRTP supported
  When client is not “local”, media goes through Mediation
    Codec optimized for WAN using per session CAC; RTANB over internet
    Mediation provides audio healing
Enables “lightweight” Mediation (collocation with FE, SBA)

## Slide 30: Lync 2010: Media Bypass How it works – two approaches
“Always Bypass” in “Global Settings”
  Treats deployment as a single site, requires good connectivity
  Mutually exclusive with Call Admission Control
  Will always bypass to trunks enabled for bypass
“Use Sites and Region Configuration”
  Leverages topology information in Lync from CAC
    Uses Region/Sites definition, requires a “Bandwidth Policy Profile”
    Associates unique Bypass ID with each Region/Site
  Uses dynamic (real time) client location
    Client IP address  Bypass ID associated with client’s location
    Gateway address (for media)  Bypass ID of the gateway’s location
  Comparison of the IDs, bypass if the two IDs match

## Slide 31: Lync 2010: Media Bypass Inbound and Outbound logics
Inbound calls (to Lync)
  Mediation receives invite; IP address of media gateway in SDP
    Potentially different from centralized call management (signaling) IP
  Mediation computes gateway Bypass ID, puts it in SDP, forks invite to clients
  Client makes bypass decision
Outbound calls (from Lync)
  Client puts its Bypass ID (from inband) in SDP, sends to Mediation
  Mediation finds gateway, determines gateway Bypass ID
    Uses representative (“alternate”) media IP if configured, or uses IP associated with GW FQDN if not (signaling IP used for media – single site)
  Mediation Server compares, call is bypassed if matches

## Slide 32: Testing and Qualification for Lync Interop Open Interoperability Program
Survivable Branch Appliances qualified, all support bypass
  5 partners – Audiocodes, Dialogic, Ferrari, HP, NET
Gateways (not all support bypass – see OIP page)
  Cisco ISR series 28xx, 29xx, 38xx, and 39xx
  Avaya 23xx and 41xx
  Gateways from Media5, Nuera, and Quintum
IP-PABX (not all support bypass – see OIP page)
  Cisco 4.x, Cisco 6.1, Cisco 7.1 and Cisco 8.x
  Avaya CM/Aura 4.x, Avaya CM/Aura 5.x
  Avaya CS1k 5.x, Avaya CS1k 6.x
  Alcatel Lucent 9.x, Siemens 3.1Rx
  Mitel, Genband, Aastra, and Huawei

## Slide 33: Provisioning media bypass with CUCM 4.1.3 SR8 configuration

## Slide 34: Media Bypass with Cisco IP-PABX (CUCM) Single site
Cisco
phone
Lync
Endpoint
MTP
CUCM
G.711
Lync (w/ Mediation Service)

## Slide 35: Step 1: setting up Lync for media bypass interop
Review topology in topology builder
Run Powershell script to:
  Create trunk and build route
  Create number normalization
  Assign policies
Verify script results in Lync Control Panel

## Slide 36: Step 2: setting up CUCM for media bypass interop
Configure MTP recourses
Create trunk
Create route pattern and associate to trunk
Set partition and CSS (optional)
Create translation rules (optional)

## Slide 37: CUCM Configuration – SIP Trunk

## Slide 38: CUCM Configuration – Route Pattern

## Slide 39: Media Bypass – Signaling Multiple Sites, Centralized - What’s different
Centralized IP-PABX with multiple sites
  IP-PABX centralized in HQ for signaling and call control
    Mediation talks to centralized instance
  Local media gateways in branch sites (ex: Cisco ISR with MTP)
    Want to bypass media to local gateway when Lync is in the branch site
Lync supports media bypass in multiple sites
  Define regions and sites in network topology (same as CAC)
  Define (virtual) media gateways in topology builder
    Associate representative media IP in site to each media gateway
    Depending on specific IP-PABX requirements, different listening ports
  Establish appropriate routing on both systems
    IP-PABX unaware of Lync dynamic location; suggest routing to local trunk

## Slide 40: Media Bypass with CUCM In-branch call between Lync endpoint and Cisco phone via branch MTP
CUCM
Lync
Mediation
PSTN
PABX
Endpoint
Lync
Endpoint
Lync
Endpoint
Gateway
WAN
Cisco
phone
ISR (MTP)
G.711
HQ Site
Branch

## Slide 41: Media Bypass with CUCM In-branch call between Lync endpoint and Cisco phone via branch MTP
CUCM
Lync
Mediation
PSTN
PABX
Endpoint
Lync
Endpoint
Lync
Endpoint
Gateway
WAN
Cisco
phone
ISR (MTP)
G.711
HQ Site
Branch
Call stays up

## Slide 42: No Media Bypass for Calls on WAN WAN call between Lync in branch and Cisco phone via central MTP
CUCM
Lync
Mediation
PSTN
PABX
Endpoint
Lync
Endpoint
Lync
Endpoint
Gateway
WAN
Cisco
phone
ISR (MTP)
HQ Site
Branch
G.711
RT Audio Narrowband

## Slide 43: No Media Bypass for Calls on WAN WAN call between Lync in branch and PSTN GW in central location
CUCM
Lync
Mediation
PSTN
PABX
Endpoint
Lync
Endpoint
Lync
Endpoint
Gateway
WAN
Cisco
phone
ISR (MTP)
HQ Site
Branch
G.711
RT Audio Narrowband

## Slide 44: Media Bypass with IP-PABX Branch call with local resiliency
CUCM
Lync
Mediation
PSTN
PABX
Endpoint
Lync
Endpoint
Lync
Endpoint
Gateway
WAN
Cisco
phone
ISR (MTP)
HQ Site
Branch
Lync SBS
G.711

## Slide 45: Migration approaches

## Slide 46: A migration and coexistence plan with CUCM and ISR
Topology with CUCM and ISR
ISR used as GW by both CUCM and Lync
    Used for PSTN calls by both “PABX”
    Including media bypass to ISR
Direct SIP between CUCM and Lync
    Used for extension calls by both “PABX”
    Including media bypass to CUCM
Migrate users stepwise
CUCM
ISR (MTP)
Lync

## Slide 47: A migration and coexistence plan with CUCM and ISR

## Slide 48: An alterative migration approach
Qualified Gateway
The gateway can do AD lookup
  Enable easy migration
  Can fork call
SIP to PABX not mandatory
Minimize PABX configuration and maintains
IP-PABX
Lync
PSTN
Gateway
AD

## Slide 49: Takeaway
Deep Video Integration through Open Interop Program
Integrating natively with IP-PABXs can
  Enable a low cost Proof of Concept
  Provide calling between migrated and non-migrated users
  Allow for long term coexistence with existing IP-PABX starting to take advantage of Lync
Native integration with media bypass enables
  CPE-less deployment of Lync in branches coexisting with existing IP-PABX, using existing equipment
  Keeping much more of the media local, including in centralized multisite topologies

## Slide 50: Enrol in Microsoft Virtual Academy Today
Why Enroll, other than it being free?
The MVA helps improve your IT skill set and advance your career with a free, easy to access training portal that allows you to learn at your own pace, focusing on Microsoft technologies.
What Do I get for enrolment?
Free training to make you become the Cloud-Hero in my Organization
Help mastering your Training Path and get the recognition
Connect with other IT Pros and discuss The Cloud
Where do I Enrol?
www.microsoftvirtualacademy.com
Then tell us what you think. TellTheDean@microsoft.com

## Slide 51: Resources
www.msteched.com/Australia
  Sessions On-Demand & Community
http:// technet.microsoft.com/en-au
  Resources for IT Professionals
http://msdn.microsoft.com/en-au
  Resources for Developers
www.microsoft.com/australia/learning
Microsoft Certification & Training Resources

## Slide 52
© 2010 Microsoft Corporation. All rights reserved. Microsoft, Windows, Windows Vista and other product names are or may be registered trademarks and/or trademarks in the U.S. and/or other countries.
The information herein is for informational purposes only and represents the current view of Microsoft Corporation as of the date of this presentation. Because Microsoft must respond to changing market conditions, it should not be interpreted to be a commitment on the part of Microsoft, and Microsoft cannot guarantee the accuracy of any information provided after the date of this presentation. MICROSOFT MAKES NO WARRANTIES, EXPRESS, IMPLIED OR STATUTORY, AS TO THE INFORMATION IN THIS PRESENTATION.