## Slide 2: iSCSI: Getting Best Performance, High-Availability & Virtualization
Rick Claus
Sr. Technical Evangelist
Microsoft Canada, eh?
rick.claus@microsoft.com
Twitter: RicksterCDN
SESSION CODE: SRV/VIR308

## Slide 3: To Begin, A Poll…
What’s the best SAN for business today?
  Fibre Channel?
  iSCSI?
  Fibre Channel over Ethernet?
  Infiniband?
  An-array-of-USB-sticks-all-linked-together?
Studies suggest the answer to this question doesn’t matter…

## Slide 4: The Storage War is Over & Everybody Won
An EMC Survey from 2009 found that…
  Selected SAN medium does not appear to be based on virtual platform.
  While this study was virtualization-related, it does suggest one thing…
Source: http://www.emc.com/collateral/ analyst-reports/2009-forrester-storage-choices -virtual-server.pdf

## Slide 5: iSCSI, the Protocol. iSCSI, the Cabling.
iSCSI’s Biggest Detractors
  Potential for oversubscription
  Less performance for some workloads
  TCP/IP security concerns
    E.g., you just can’t hack a strand of light that easily…
iSCSI’s Biggest Benefits
  Reduced administrative complexity
  Existing in-house experience
  (Potentially) lower cost
  Existing cabling investment and infrastructure

## Slide 6: iSCSI: Easy Enough for a Ten Year Old…Easy Enough for You!
Video

## Slide 7: Network Accelerations in Server 2008 & R2
TCP Chimney Offload
  Transfers TCP/IP protocol processing from the CPU to network adapter.
  First available Server 2008 RTM, R2 adds automatic mode and new PerfMon counters.
  Often an extra licensable feature in hardware, with accompanying cost.
Virtual Machine Queue
  Distributes received frames into different queues based on target VM. Different CPUs can process.
  Hardware packet filtering to reduce the overhead of routing packets to VMs.
  VMQ must be supported by the network hardware. Typically Intel NICs & Procs only.
Receive Side Scaling
  Distributes load from network adapters across multiple CPUs.
  First available in Server 2008 RTM, R2 improves initialization and CPU selection at startup, adds registry keys for tuning performance, and new PerfMon counters.
  Most server-class NICs include support.
NetDMA
  Offloads the network subsystem memory copy operation to a dedicated DMA engine.
  First available in Server 2008 RTM, R2 adds no new capabilities
Acceleration features were available in Server 2003’s Scalable Networking Pack.
Server 2008 & R2 now include these in the OS.
However, ensure your NICs support them!

## Slide 8: Getting Better Performance & Availability
Big Mistake #1: Assuming NIC Teaming = iSCSI Teaming
  NIC Teaming is common in production networks
  Leverages proprietary driver from NIC manufacturer
  However, iSCSI teaming requires MPIO or MCS
  These are protocol-driven, not driver-driven.

## Slide 9: Getting Better Performance & Availability
MCS = Multiple Connections per Session
  Operates at the iSCSI Initiator level.
  Part of the iSCSI protocol itself.
  Enables multiple, parallel connections to target.
  Does not require special multipathing technology for manufacturer.
  Does require storage device support.

## Slide 10: Getting Better Performance & Availability
MCS = Multiple Connections per Session
  Configured per-session and applies to all LUNs exposed to that session.
  Individual sessions are given policies.
    Fail Over Only
    Round Robin
    Round Robin with a subset of paths
    Least Queue Depth
    Weighted Paths

## Slide 11: Multiple Connections per Session
demo

## Slide 12: Getting Better Performance & Availability
MPIO = Multipath Input/Output
  Same functional result as MCS, but with different approach.
    Manufacturers create MPIO-enabled drivers.
    Drivers include Device Specific Module that orchestrates requests across paths.
    A single DSM can support multiple transport protocols (such as Fibre Channel & iSCSI).
    You must install and manage DSM drivers from your manufacturer.
    Windows includes a native DSM, not always supported by storage.

## Slide 13: Getting Better Performance & Availability
MPIO = Multipath Input/Output
  MPIO policies are applied to individual LUNs. Each LUN gets its own policy.
    Fail Over Only
    Round Robin
    Round Robin with a subset of paths
    Least Queue Depth
    Weighted Paths
    Least Blocks
  Not all storage supports every policy!

## Slide 14: Multipath I/O
demo

## Slide 15: Which Option to Choose?
Many storage devices do not support the use of MCS.
  In these cases, your only option is to use MPIO.
Use MPIO if you need to support different load balancing policies on a per-LUN basis.
  This is suggested because MCS can only define policies on a per-session basis.
  MPIO can define policies on a per-LUN basis.
Hardware iSCSI HBAs tend to support MPIO over MCS.
  Not that many of us use hardware iSCSI HBAs…
  But if you are, you’ll probably be running MPIO.
MPIO is not available on Windows XP, Windows Vista, or Windows 7.
  If you need to create iSCSI direct connections to virtual machines, you must use MCS.
MCS tends to have marginally better performance over MPIO.
  However, it can require more processing power. Offloads reduce this impact.
  This may a negative impact in high-utilization environments.
  For this reason, MPIO may be a better selection for these types of environments.

## Slide 16: Better Hyper-V Virtualization
iSCSI for Hyper-V best practices suggest using network aggregation and segregation.
  Aggregation of networks for increased throughput and failover.
  Segregation of networks for oversubscription prevention.

## Slide 17: Single Server, Redundant Connections
Legend:
Storage network
Production network

## Slide 18: Single Server, Redundant Path
Legend:
Storage network
Production network

## Slide 19: Hyper-V Cluster, Minimal Configuration
Legend:
Cluster Network
Storage network
Production network

## Slide 20: Hyper-V Cluster, Minimal Redundancy
Note the separate management connection for segregation of security domains and/or Live Migration traffic.
Legend:
Cluster Network
Storage network
Production network
Management / LM

## Slide 21: Hyper-V Cluster, Maximum Redundancy
10Gig-E and VLANs significantly reduce physical complexity.
Legend:
Cluster Network
Storage network
Production network
Management / LM

## Slide 22: Hyper-V iSCSI Disk Options
Option #1: Fixed VHDs
  Server 2008 RTM: ~96% of native
  Server 2008 R2: Equal to Native
Option #2: Pass Through Disks
  Server 2008 RTM: Equal to Native
  Server 2008 R2: Equal to Native
Option #3: Dynamic VHDs
  Server 2008 RTM: Not a great idea
  Server 2008 R2: ~85%-94% of native

## Slide 23: Which to Use?
VHDs are believed to be most commonly used option.
  Particularly in the case of System drives.
Choose Pass Through Disks not necessarily for performance, but VM workload requirements.
  Backup and recovery
  Extremely large volumes
  Support for storage management software
  App Compat requirement for unfiltered SCSI.

## Slide 24: Hyper-V iSCSI Option #4
iSCSI Direct
  Essentially, connect a VM directly to an iSCSI target.
  Hyper-V host does not participate in connection.
  VM LUN not visible to Hyper-V host.
  VM LUNs can be hot added/removed without requiring reboot.
  Transparent support for VSS hardware provider.
  Enables guest clustering.
Potential concern…
  Virtually no degradation in performance.
  Some NIC accelerations not pulled into VM.

## Slide 25: Demartek Test Lab – Hyper-V
Comparison of 10Gb iSCSI performance
  Native server vs. Hyper-V guest, iSCSI direct
  Same iSCSI target & LUNs (Windows iSCSI Storage Target)
  Exchange Jetstress 2010: mailboxes=1500, size=750MB, Exchange IOPS=0.18, Threads=2
 | Native | iSCSI Direct
Achieved IOPS | 519.816 | 464.12
Database Read Average Latency | 9.459 msec. | 11.909 msec.
Log Write Average Latency | 8.236 msec. | 9.732 msec.

## Slide 26: Demartek Test Lab – 10Gb iSCSI Performance
Perfmon trace of single-host Exchange Jetstress to fast Windows iSCSI storage target consuming 37% of 10Gb pipe

## Slide 27: Demartek Test Lab – Jumbo Frames
Jumbo Frames allow larger packet sizes to be transmitted and received
Jumbo Frames testing has yielded variable results
  All adapters, switches and storage targets must agree on size of jumbo frame
  Some storage targets do not fully support jumbo frames or have not tuned their systems for jumbo frames – check with your supplier

## Slide 28: Demartek Test Lab – 1Gb vs. 10Gb iSCSI
10GbE adoption is increasing
  Server Virtualization is a big driver
    Not too difficult for one host to consume a single 1GbE pipe
    Difficult for one host to consume a single 10GbE pipe
  SSD adoption in storage targets increases performance of the storage and can put higher loads on the network
  Big server vendors are beginning to offer 10GbE on server motherboards

## Slide 29: Demartek Test Lab – iSCSI
Demartek Lab video of ten-year old girl deploying iSCSI on Windows 7: www.youtube.com/Demartek
Demartek iSCSI Zone: www.demartek.com/iSCSI
  Includes more test results
  The Demartek iSCSI Deployment Guide 2011 will be published this month

## Slide 30: Final Thoughts
Server 2008 R2 adds significant performance improvements to iSCSI storage.
  Hardware accelerations and MPIO improvements
  Hyper-V enhancements
Configuring iSCSI is easy, if…
  Keep network aggregation and separation in mind.
  Avoid the most common mistakes.
  Get on 10Gig-E as soon as you can!

## Slide 31: Q and
Rick Claus
Sr. Technical Evangelist
Microsoft Canada
rick.claus@microsoft.com
Twitter: RicksterCDN
SESSION CODE: SRV305
eh?
A?
X

## Slide 32: Enrol in Microsoft Virtual Academy Today
Why Enroll, other than it being free?
The MVA helps improve your IT skill set and advance your career with a free, easy to access training portal that allows you to learn at your own pace, focusing on Microsoft technologies.
What Do I get for enrolment?
Free training to make you become the Cloud-Hero in my Organization
Help mastering your Training Path and get the recognition
Connect with other IT Pros and discuss The Cloud
Where do I Enrol?
www.microsoftvirtualacademy.com
Then tell us what you think. TellTheDean@microsoft.com

## Slide 33
© 2010 Microsoft Corporation. All rights reserved. Microsoft, Windows, Windows Vista and other product names are or may be registered trademarks and/or trademarks in the U.S. and/or other countries.
The information herein is for informational purposes only and represents the current view of Microsoft Corporation as of the date of this presentation. Because Microsoft must respond to changing market conditions, it should not be interpreted to be a commitment on the part of Microsoft, and Microsoft cannot guarantee the accuracy of any information provided after the date of this presentation. MICROSOFT MAKES NO WARRANTIES, EXPRESS, IMPLIED OR STATUTORY, AS TO THE INFORMATION IN THIS PRESENTATION.