## Slide 2: Migrating to IPv6 with Windows Server 2008 R2 and Windows 7
Freddie Louwrens
System Consultant
Stratbits Consulting
SESSION CODE: SVR413

## Slide 3: Three Questions
  What does 0 mean?
  What does 340,282,366,920,938,463,463,374,607,431,768,211,456 mean?
  The total IPv4 numbers that IANA has
  Total IPv6 numbers
  Has anyone played with IPv6?
  Please raise your hands

## Slide 4: IPv6 Refresh
Unicast Address | Description
Link Local | The scope of the IPv6 address is the local subnet. IPv6 link local addresses are comparable to IPv4 link local addresses used in Automatic Private IP Addressing
Global | The scope of the IPv6 address is the whole world. IPv6 global addresses are comparable to IPv4 public IP addresses

## Slide 5: IPv6 Refresh
Item | IPv4 | IPv6
Private IP Address | 10.0.0.0/8 172.16.0.0/16 192.168.0.0/24 | FD00::/8
Link Local Address | 169.254.0.0/16 | FE80::/64
Loopback Address | 127.0.0.1 | ::1
Unspecified Address | 0.0.0.0 | ::
Address Resolution | ARP | Neighbour Discovery (ND)
DNS Host Name Resolution | A Record | AAAA Record or A6 Record

## Slide 6: Agenda
The 5 steps to IPv6
Migrating Windows Operating System
Migrating an application server
  IIS 7.0
  Exchange 2010
Running into problems
  Firewall
  Windows 7 random IP number

## Slide 7: The 5 Steps to IPv6
Step 1 IPv6 Design
  Subnets
    You get /48
      Example: 2001:1310:1969::/48
    You can make 65536 subnets
      Example 1: On subnet for each vlan:
      2001:1310:1969:0001::/64
      Example 2: On subnet for each location:
      2001:1310:1969:107A::/64 (4218=107A)

## Slide 8: The 5 Steps to IPv6
Step 1 IPv6 Design
  Number
    You have 64 bits
    You have 4 times 16 bits
  Some examples
    Server001 = 2001:1310:1969:2:0:0:A:001
    Workstations = 2001:1310:1969:2:0:0:B:/64
    RoutersA = 2001:1310:1969:2:0:0:B:A/64

## Slide 9: The 5 Steps to IPv6
Step 1 IPv6 Design
  Router
    Global range
    IPv6 over IPv4
      ISATAP
      Teredo
      6to4
  Prefix discovery
    DHCPv6
    Router

## Slide 10: The 5 Steps to IPv6
Step 1: IPv6 Design
Keep it simple
Design for growth
  Work with /48, /52, /56, /60 or /64

## Slide 11: The 5 Steps to IPv6
  Network devices
  Operating Systems
  Applications
Step 2: IPv6 Readiness
IPv6 Ready Logo Program
www.ipv6ready.org

## Slide 12: The 5 Steps to IPv6
Step 3: IPv6 Testing
  IPv6 network device
  IPv6 Application
  IPv6 User

## Slide 13: The 5 Steps to IPv6
Step 4: Dual Stack
Step 5: Bye Bye IPv4

## Slide 14: Agenda
The 5 steps to IPv6
Migrating Windows Operating System
Migrating an application server
  IIS 7.0
  Exchange 2010
Running into problems
  Firewall
  Windows 7 random IP number

## Slide 15: The 5 Steps to IPv6
  Step 1
  Step 2
  Step 3
  Step 4
  Step 5
  Design
  IPv6 Ready
  IPv6 Testing
  Dual stack
  Bye Bye IPv4

## Slide 16: Demo Environment
TEAU11-INET1
TEAU11-TMG01
TEAU11-EDGE
TEAU11-DC
TEAU11-APP1
TEAU11-Win7
131.107.0.0/24
10.0.0.0/24
http://social.technet.microsoft.com/wiki/contents/articles/test-lab-guides.aspx

## Slide 17: Step 1: Design
2001:1310:1969::/48
2001:1310:1969:1::/64
Router Advertisement for the prefix
DHCPv6 for DNS Suffix and IPv6 number
131.107.0.0/24
2001:0:0:2::/64
10.0.0.0/24
2001:1310:1969:1::/64

## Slide 18: Windows Operating System IPv6 Readiness
Date | Phase | Name | Version
2004/03/26 | Phase 1 | Windows | Server 2003
2004/12/10 | Phase 1 | Windows | CE 4.2
2007/03/20 | Phase 1 | Microsoft Windows Vista | Version 6.0 (Build 6000)
2007/10/25 | Phase 2 | Microsoft Windows Vista | Version 6.0 (Build 6000)
2008/01/11 | Phase 2 | Microsoft Windows Vista | Version 6.0 (Build 6000)
2008/01/18 | Phase 2 | Microsoft Windows Server 2008 | Version 6.0.6001
2008/03/24 | Phase 2 | Microsoft Windows Server 2008 | Version 6.0.6001
2010/10/18 | Phase 2 | Windows 7 | Windows 7
Step 2 IPv6 Readiness

## Slide 19: Windows Operating System IPv6 Readiness
Windows 7 and Windows 2008 R2
Phase 2
IPv6
Neighbor Discovery for IP Version 6
  IPv6 Stateless Address Autoconfiguration
  DHCPv6 Client
  Internet Control Message Protocol for the Internet Protocol Version 6 (ICMPv6)
IPSec for IPv6

## Slide 20: Windows Operating System IPv6 Readiness
Windows 2008 R2
  DHCPv6 Service
  DNS support for IPv6
    AAAA
    IPv6 PTR

## Slide 21: Windows Operating System IPv6 Readiness
Getting a number
IPv6 Numbers: The idea
  Lets use a the MAC address for the Host ID
Prefix
  Router
  DHCPv6
00-C0-9F-2C-25-44
fe80::2c0:9fff:fe2c:2544
00C0-9F 2C-2544
Insert “fffe” and flip a bit (EUI-64)

## Slide 22: Windows Operating System IPv6 Readiness
TCP/IP Stack Before Windows Vista
NDIS
IPv4
802.3
WLAN
Loop-back
RAW
UDP
TCP
Winsock
802.3
WLAN
Loop-back
IPv4 Tunnel
IPv6 Tunnel
IPv6
RAW
UDP
TCP

## Slide 23: Windows Operating System IPv6 Readiness
Next Generation TCP/IP Stack (Window Vista and newer)
NDIS
Winsock
IPv4
802.3
WLAN
Loop-back
IPv4 Tunnel
IPv6 Tunnel
IPv6
RAW
UDP
TCP

## Slide 24: Windows Operating System IPv6 Readiness
Windows 7
  IPv6 Address
    Random
    “Normal” live time
  Temporary IPv6 Address
    Random
    Relatively short valid lifetime (RFC 3041)

## Slide 25: Demo
Enable Router Advertisement on Windows 2008 R2

## Slide 26: Windows Operating System IPv6 Readiness
The Commands
Microsoft Windows [Version 6.1.7600]
Copyright (c) 2009 Microsoft Corporation. All rights reserved.
C:\Netsh interface IPv6 Set Interface 18 Advertise=enabled
OK
C:\Netsh interface IPv6 Set route 2001:1310:1969:1::/64 interface=18 publish=yes
OK
C:\Netsh interface IPv6 Set route::/0 interface=19 publish=yes
OK
c:\Netsh interface IPv6 set interface 18 ManagedAddress=Disabled
OK
C:\

## Slide 27: Agenda
The 5 steps to IPv6
Migrating Windows Operating System
Migrating an application server
  IIS 7.0
  Exchange 2010
Running into problems
  Firewall
  Windows 7 random IP number

## Slide 28: Application IPv6 Readiness
Physical
Datalink
Transport
Session
Presentation
Application
Network
IPv4
IPv6

## Slide 29: Application IPv6 Readiness
Physical
Datalink
Transport Socket
Session Session based on IP#
Presentation
Application IP# in application
Network
IPv4
IPv6

## Slide 30: Application IPv6 Readiness
Theory
  Only the network layer
Read World
  Sockets
    192.168.1.1:80  [2001:1310:1969:1::1]:80
  Monitoring/logfiles
    Field size: 32 bits?
    Field type: IPv4 field
  Security
    Allow or block IPv4 and IPv6 numbers

## Slide 31: Internet Information Server 7.0 & 7.5
Binding
  HTTP
  HTTPS
IP Address and Domain Restrictions
Logging
FTP

## Slide 32: Exchange 2010 and IPv6
Source | Feature | IPv6 supported
Transport | IP Allow list and IP Block list | Yes
Transport | Sender ID | Yes
Transport | Receive connectors | Yes
Transport | Send connectors | Yes
Mailbox (Database availability group member) | IPv6 addresses | Yes
Features That Works

## Slide 33: Exchange 2010 and IPv6
Source | Feature | IPv6 supported
Transport | IP Allow List providers and IP Block List providers | No
Transport | Sender reputation | No
Transport | Incoming message rate limits | Partial (only global IPv6)
Unified Messaging | All features | No
Features That Don’t Works
http://technet.microsoft.com/en-us/library/gg144561.aspx

## Slide 34: Demo
Migrate a website to IPv6

## Slide 35: Agenda
The 5 steps to IPv6
Migrating Windows Operating System
Migrating an application server
  IIS 7.0
  Exchange 2010
Running into problems
  Firewall
  Windows 7 random IP number

## Slide 36: Solve the IPv6 problem
Disable IPv6
  HKLM\SYSTEM\CurrentControlSet\Services\Tcpip6\Parameters\
    Disabled Components
Hyper-V cluster
  It is not possible to add a new node to an existing cluster
TMG server
  RRAS breaks
Exchange
  Mailflow problems
  Installing problems
  Services fail
Direct Access
  Does not work
HomeGroup
  Does not work

## Slide 37: Solve the IPv6 problem
Implement IPv6
Step 1: Design
Step 2: IPv6 Ready
Step 3: IPv6 Testing
Step 4: Dual stack

## Slide 38: Solve the IPv6 problem
What if there is no solution
  No IPv6 Firewall
  No IPv6 sockets
  Wrong logging
Force the use of IPv4
  Dual Stack

## Slide 39: Troubleshooting IPv6
Demo
Forefront Threat Management Gateway

## Slide 40: Troubleshooting IPv6
Demo
Windows 7 random numbers

## Slide 41: Helpful Resources
TCP/IP Fundamentals for Microsoft Windows (Whitepaper)
Understanding IPv6 Second Edition - Joseph Davies
Migrating to IPv6: A Practical Guide to Implementing IPv6 in Mobile and Fixed Networks
IPv6 Network Administration - Niall Richard Murphy & David Malone
IPv6 Essentials - Silvia Hagen

## Slide 42: Agenda
The 5 steps to IPv6
Migrating Windows Operating System
Migrating an application server
  IIS 7.0
  Exchange 2010
Running into problems
  Firewall
  Windows 7 random IP number

## Slide 43: Q&A
Keep in mind:
IPv6 = IPv4 but then 128 bits ;-)
131.107.0.1
10000011.01101011.00000000.00000001
2001:1310:1969:1:0:0:0:1
0010000000000001:0001001100010000:0001100101101001:0000000000000001:0000000000000000:0000000000000000:0000000000000000:0000000000000001
340- undecillion,
282- decillion,
366- nonillion,
920- octillion,
938- septillion,
463- sextillion,
463- quintillion,
374- quadrillion,
607- trillion,
431- billion,
768- million,
211- thousand,
456

## Slide 44: Track Resources
Don’t forget to visit the Cloud Power area within the TLC (Blue Section) to see product demos and speak with experts about the Server & Cloud Platform solutions that help drive your business forward.
You can also find the latest information about our products at the following links:
Windows Azure - http://www.microsoft.com/windowsazure/
Microsoft System Center - http://www.microsoft.com/systemcenter/
Microsoft Forefront - http://www.microsoft.com/forefront/
Windows Server - http://www.microsoft.com/windowsserver/
Cloud Power - http://www.microsoft.com/cloud/
Private Cloud - http://www.microsoft.com/privatecloud/

## Slide 45: Enrol in Microsoft Virtual Academy Today
Why Enroll, other than it being free?
The MVA helps improve your IT skill set and advance your career with a free, easy to access training portal that allows you to learn at your own pace, focusing on Microsoft technologies.
What Do I get for enrolment?
Free training to make you become the Cloud-Hero in my Organization
Help mastering your Training Path and get the recognition
Connect with other IT Pros and discuss The Cloud
Where do I Enrol?
www.microsoftvirtualacademy.com
Then tell us what you think. TellTheDean@microsoft.com

## Slide 46
© 2010 Microsoft Corporation. All rights reserved. Microsoft, Windows, Windows Vista and other product names are or may be registered trademarks and/or trademarks in the U.S. and/or other countries.
The information herein is for informational purposes only and represents the current view of Microsoft Corporation as of the date of this presentation. Because Microsoft must respond to changing market conditions, it should not be interpreted to be a commitment on the part of Microsoft, and Microsoft cannot guarantee the accuracy of any information provided after the date of this presentation. MICROSOFT MAKES NO WARRANTIES, EXPRESS, IMPLIED OR STATUTORY, AS TO THE INFORMATION IN THIS PRESENTATION.

## Slide 47: Resources
www.msteched.com/Australia
  Sessions On-Demand & Community
http:// technet.microsoft.com/en-au
  Resources for IT Professionals
http://msdn.microsoft.com/en-au
  Resources for Developers
www.microsoft.com/australia/learning
Microsoft Certification & Training Resources