## Slide 2: TechEd Backstage 2011 www.techedbackstage.net
David Connors
Managing Director
Codify Pty Ltd
david@codify.com @davidconnors
SESSION CODE: VOC203
TWITTER HASH TAG: #VOC203
Ben Parker
Infrastructure Consultant
Codify Pty Ltd
ben@codify.com
@parker_ben

## Slide 3: Agenda Building a 3000+ person enterprise in 3 weeks
General Overview: Who are you?
How’s our driving: Facts and Figures from 2011
PART 1: TCP/IP Performance and getting your bucks worth
PART 2: cloud.auteched.net
  Hardware
  Network services and vlan provisioning
  VMM 2012

## Slide 4: Who’s who in the zoo
Lots of vendors (80?)
Relevant to this talk:
  JMW = MS global AoR for events
  Jomablue = Logistics & project management for technology (and nagging)
  Codify = Infrastructure engineering and propelloryhead bits

## Slide 5: Wins
Keynote
  ~900 concurrent wifi clients + 1-2ms pings back to GigabitEthernet1-8.cha30.Brisbane.telstra.net at the same time
Current wifi peak: 1781 concurrent
IP transit: Very fast/diverse
~200 session VMs provisioned for sessions on-demand
~12 private networks provisioned across the building on-demand for sessions
0 network faults (touch melamine)

## Slide 6: IP Transit Providers
Telstra – Premier Sponsor
  Telstra Internet Direct Service
  1000mbps e-line terminating at Telstra CHA exchange
  IPv4
Over The Wire – Plan B in case something goes sproing
  Pipe Networks fibre terminating at Pipe DC2
  500mbps
  IPv4 + IPv6

## Slide 7: Wifi
Australian Partner Conference 2011
TechEd 2011
Tuesday Keynote
871 associations
Thursday Peak
1781 associations

## Slide 8: random wifi dissassociations
20-40 random disassociations/sec (for < 10ms)
Resolved just prior to APC with Cisco TAC (firmware upgrade with no fixes in the release notes O_o)

## Slide 9: Other random IP bits
IPv4 – None left, we are all going to die…
  Dear David,
  Thank you for your email reply.
  There is no IPv4 address space available for temporary allocation.
  [ ... blah blah blah ... ]
  Kind Regards
  Tom Do Internet Resource Analyst, APNIC
BGP Routing
  aut-num: AS9984 as-name: MICROSOFT-TECHED-AS-AP descr: Microsoft Tech Ed Australia 2011 descr: for Microsoft Tech Ed conference descr: http://australia.msteched.com/ descr: Gold Coast Convention and Exhibition Centre descr: Cnr Gold Coast Highway & T.E. Peters Drive descr: Broadbeach descr: Queensland 4218 country: AU
IPv6 again – standard operating procedure now

## Slide 11
WHY???
WHY???
WHY???
WHY???

## Slide 12: Part 1
IP Transit – Getting what you paid for.

## Slide 13: IP Transit: What we want
Great performance for typical usage scenarios
Significantly exceed commonly expected performance
Delegeeks (and APC sales drones) must ♥ the APC/TechEd network
Matter of brand value for Microsoft
Matter of pride for the TechOps team

## Slide 14: A few primers
Ethernet: Chuck data at a wall and see what sticks
  IEEE 802.3 is CSMA/CA
  Simple and clever design  Self-clocking
  Useless if congested
Internet Protocol Suite
  The Internet is powered by a suite of protocols
  Different protocols support different usage scenarios

## Slide 15: TCP congestion management
Works like magic!
Have you noticed downloading a file and the transfer starts off slow then speeds up?
This is congestion management at work.
Not very deterministic but the Internet wouldn’t work otherwise.

## Slide 16: Typical Internet Usage Scenario
www.4chan.org
10gbps
Some Fancy IP Transit Provider
80mbps
Some Dodgy IP Transit Provider
10gbps
ISP core
10gbps
Some Fancy IP Transit Provider
10gbps
Some Fancy IP Transit Provider
10gbps
ISP core
1gbps
1gbps
10mbps
0.8mbps
Resi-grade DSL “Router”
Data centre cross-connect
161 millisecond round-trip time
Some observations:
The trip from AB is on a different path to BA
Couple of dodgy providers in the mix – How do we stop the 80mbps and 10mbps links on the red path getting smashed?
In reality there are 15 hops between us an 4chan
Ye cannay change the laws of physics

## Slide 17: How TCP doesn’t work
www.4chan.org
161 millisecond round-trip time
HTTP Request for naked picture of Miranda Kerr
Old-mate just had a disappointing user experience
ACK
ACK
ACK

## Slide 18: How TCP DOES work
www.4chan.org
161 millisecond round-trip time
HTTP Request for naked picture of Miranda Kerr
Old-mate just had an AWESOME user experience
ACK
ACK
ACK
ACK
TCP tunes itself to make use of bandwidth without smashing links
Latency affects the number of packets that can be in flight at once
This is called the bandwidth delay product (BDP)
All of this is true but it is not a get out of jail free card for performance problems

## Slide 19: Common myths
EVERY supplier uses BDP as an excuse
iperf and UDP are their weapons of choice
  Great if DNS was the primary use case for perf #fail
  Most deep packet inspection happens on TCP streams (i.e. you’ll find traffic policing issues there)
Get a BDP calculator and tell them to get back in their box

## Slide 20: Bestest excuses ever
“Ping is irrelevant for measuring latency! It is a UDP protocol!”
  Anonymous muppet at TechEd 2011

## Slide 21: Bestest excuses ever
“You can’t use FTP for bandwidth testing because it is adaptive”
  ISP on Hamilton Island

## Slide 22: Bestest excuses ever
[ Walks in with a smashed Netcomm NB9 resi-grade DSL modem with an antenna hanging out the back ]
“I am here to install your 6 meg link”.

## Slide 23: Bestest excuses ever
2 am, pouring rain in the middle of a golf course
Linesman turns up
“I am here to fix a problem with an ATM.”
CAN YOU SPOT THE DIFFERENCE?

## Slide 24: #1 Bestestestiest excuse ever
Name server returns NXDOMAIN RCODE for a domain the delegates rely on
“Could be due to hurricane Irene.”

## Slide 25: Part 2
cloud.auteched.net

## Slide 26: DemoNet What is it?
Private cloud supporting demonstrations during the event
Showcase latest MS and HP technology
Sitting in the middle of the Expo hall

## Slide 27: DemoNet Stats
28 of clouds
  238 VMs
  9 hosts dedicated to session
  8 networks (+reuse)

## Slide 28: DemoNet How do you get on it?
Communicated during Speaker registration
Capture requirements upfront
VMs imported on-site, via USB HDD
Capture requirements (again)

## Slide 29: DemoNet The conditions in which we work
Unstable environmental conditions
  Power outs
  Muppets with pliers
  People kicking over beers
Layout vs. purpose
  Showcase not really a data centre
Physical access

## Slide 32: DemoNet Logistics
SYD/SIN > BNE
  Codify HQ (2nd August)
  Environment build (firmware, OS, core infra)
  Hosted on same IP space as event before going on site
BNE > GCCEC
  Showcase
  Go-live (Friday 26th August)
  Plug it in and it ‘just works’

## Slide 33: DemoNet Logistics
Showcase hardware unpacking in action

## Slide 34: DemoNet Design rational
Highest level resilience for the environment
  Hyper-V Clusters
  Failover network design
  Storage RAID6 (not RAID0)
  Power – Single 32A 3phase
Shared Services

## Slide 35: DemoNet Hardware
24 x HP BL460c G7 (4 Enclosures, 2 Racks)
  ServerEngines and Virtual Connect
HP EVA HSV300
  45 x SAS 450 GB
  11 x FATA 1 TB
  79% allocated

## Slide 36: DemoNet Hardware
DEMO

## Slide 37: DemoNet Hardware (cont.)

## Slide 38: DemoNet Management
SCVMM 2012 Beta
  Bare Metal Builds
    WinPE + HP SmartStart + WDS
    Windows 2008 R2
    Enable Hyper-V role
    Proliant Support Pack (HP NCU)
    SAN tools/mgmt

## Slide 39: DemoNet Management
SCVMM 2012 Beta
  VM templates
    WIM2VHD + unattend.xml
  SSP